## Slide 1: Titolo presentazione sottotitolo
Milano, XX mese 20XX
EMBEDDED SYSTEMS PROJECT
Maitan, Medvedec, Megler, Paone

## Slide 2: OUTLINE
INTRODUCTION
HARDWARE
  GPIO
  TIMER
  INTERRUPT
SOFTWARE
  DECODING
  ENCRYPTING
  ENCODING
TESTBENCH

## Slide 3: INTRODUCTION
The project addresses the problem of encryption of a plain text in microcontroller based application.
The core of application is thus composed of three main tasks:
Acquire plain text in input
Generate cipher-text with the Caesar cipher
Display in output the outcome of the encryption

## Slide 4: INTRODUCTION
The project addresses the problem of encryption of a plain text in microcontroller based application.
The core of application is thus composed of three main tasks:
Acquire plain text in input  HARDWARE
  Provide the Morse message using push-buttons on the board
Generate cipher-text with the Caesar cipher  SOFTWARE
Display in output the outcome of the encryption  HARDWARE
  Output the cipher-text in Morse using LEDs

## Slide 5: HARDWARE
GPIO:
  We used the two GPIOs located on the board
    GPIO_0  communicates with LEDs
    GPIO_1  bound to the push-buttons
TIMER:
  We used the systick timer to measure the time when a button pressure occurs in order to understand if a signal is long or short

## Slide 6: HARDWARE
INTERRUPT:
  Generates a signal event that stop the normal exeution of the instruction flow
  Each GPIO has its own handler in order to react to the events
    GPIO_1 handler manages button pressure
  Systick handler is called when the timer is expired

## Slide 7: SOFTWARE
The software takes care of receiving the input characters and handling them through a “pipeline” composed by three main steps
Decoding  to build the word from Morse signals to a string compose of ASCII characters
Encrypting  takes the word and cipher it with Caesar cipher
Encoding  generates a set of Morse signals starting form the encrypted ASCII string

## Slide 8: TESTBENCH
We made several tests to check the hardaware’s behaviour with some input test
In the right picture it’s represented the code of button pressing simulation. In this case we are pushing the first button to generate the signals corresponding the ‘r’ letter, and the third button to notify that we reach the end of the character

## Slide 9: TESTBENCH

## Slide 10: TESTBENCH
UART
The sequence of frames in the UART protocol consists of :
Start / Stop bits  0/1
Data bits  binary format of character
We read the binary format of ‘u’ as the arrow says: strating from the bit before stop bit to the bit after the start bit
start 1 0 1 0 1 1 1 0 stop

## Slide 12: Firma convenzione Politecnico di Milano e Veneranda Fabbrica del Duomo di Milano
Aula Magna – Rettorato
Mercoledì 27 maggio 2015
Fare clic per modificare lo stile del titolo
Fare clic per modificare lo stile del sottotitolo dello schema
Inserimento secondo logo